## Slide 1
BGP Scalability

## Slide 2: Introduction
Will discuss various bugs we have fixed in BGP scalability
Talk about different configuration changes you can make to improve convergence
Software improvements for faster convergence

## Slide 3: Before we begin…
What does this graph show?
Shows the number of peers we can converge in 10 minutes (y-axis) given a certain number of routes (x-axis) to advertise to those peers
Example: We can advertise 100k routes to 50 peers with 12.0(12)S or 110 peers with 12.0(13)S

## Slide 4: Old Improvements
CSCdr50217 – “BGP: Sending updates slow”
Fixed in 12.0(13)S
Description
  Fixed a problem in bgp_io which allows BGP to send data to TCP more aggressively

## Slide 5: Old Improvements
What does CSCdr50217 mean in terms of scalability?
Almost 100% improvement!!

## Slide 6: Old Improvements – Peer Groups
Advertising 100,000+ routes to hundreds of peers is a big challenge from a scalability point of view. BGP will need to send a few hundred megs of data in order to converge all peers
Two part challenge
  Generating the hundreds of megs of data
  Advertising this data to BGP peers
Peer-groups make it easier for BGP to advertise routes to large numbers of peers by addressing these two problems
Using peer-groups will reduce BGP convergence times and make BGP much more scalable

## Slide 7: Peer Groups
UPDATE generation without peer-groups
  The BGP table is walked for every peer, prefixes are filtered through outbound policies, UPDATEs are generated and sent to this one peer
UPDATE generation with peer-groups
  A peer-group leader is elected for each peer-group. The BGP table is walked for the leader only, prefixes are filtered through outbound policies, UPDATEs are generated and sent to the peer-group leader and replicated for peer-group members that are synchronized with the leader
  If we generate an update for the peer-group leader and replicate it to all peer-group members we are achieving 100% replication

## Slide 8: Peer Groups
A peer-group member is “synchronized” with the leader if all UPDATEs sent to the leader have also been sent to the peer-group member
The more peer-group members stay in sync the more UPDATEs BGP can replicate. Replicating an UPDATE is much easier/faster than formatting an UPDATE. Formatting requires a table walk and policy evaluation, replication does not
A peer-group member can fall out of sync for several reasons
  *Slow TCP throughput
  **Rush of TCP Acks fill input queues resulting in drops
  Peer is busy doing other tasks
  Peer has a slower CPU than the peer-group leader

## Slide 9: Old Improvements
Peer-groups give between 35% - 50% increase in scalability

## Slide 10: Larger Input Queues
In a nutshell
  If a BGP speaker is pushing a full Internet table to a large number of peers, convergence is degraded due to enormous numbers of drops (100k+) on the interface input queue. ISP foo gets ~½ million drops in 15 minutes on their typical route reflector.
With the default interface input queue depth of 75, it takes us ~19 minutes to advertise 75k real world routes to 500 clients. The router drops ~225,000 packets (mostly TCP Acks) in this period.
By using brute force and setting the interface input queue depth to 4096, it takes us ~10 minutes to send the same number of routes to the same number of clients. The router drops ~20,000 packets in this period

## Slide 11: Larger Input Queues

## Slide 12: Larger Input Queues
Rush of TCP Acks from peers can quickly fill the 75 spots in process level input queues
Increasing queue depths (4096) improves BGP scalability

## Slide 13: Larger Input Queues
Why not change default input queue size?
  May happen someday but people are nervous
  CSCdu69558 has been filed for this issue
Even with 4096 spots in the input queue we can still see drops given enough routes/peers
Need to determine “How big is too big” in terms of how large an input queue can be before we are processing the same data multiple times

## Slide 14: MTU Discovery
Default MSS (Max Segment Size) is 536 bytes
Inefficient for today’s POS/Ethernet networks
Using “ip tcp path-mtu-discovery” improves convergence

## Slide 15: MTU Discovery and Larger Input Queues
Simple config changes can give 3x improvement

## Slide 16: UPDATE Packing
Quick review on BGP UPDATEs
An UPDATE contains:
+-----------------------------------------------------+
| Withdrawn Routes Length (2 octets) |
+-----------------------------------------------------+
| Withdrawn Routes (variable) |
+-----------------------------------------------------+
| Total Path Attribute Length (2 octets) |
+-----------------------------------------------------+
| Path Attributes (variable) |
+-----------------------------------------------------+
| Network Layer Reachability Information (variable) |
+-----------------------------------------------------+
At the top you list a combination of attributes (MED = 50, Local Pref = 200, etc)
Then you list all of the NLRI (prefixes) that share this combination of attributes

## Slide 17: Update Packing
If your BGP tables contains 100k routes and 15k attribute combinations then you can advertise all the routes with 15k updates if you pack the prefixes 100%
If it takes you 100k updates then you are achieving 0% update packing
Convergence times vary greatly depending on the # of attribute combinations used in the table and on how well BGP packs updates
Ideal Table
  Routem generated BGP table of 75k routes
  All paths have the same attribute combination
Real Table
  75k route feed from Digex (replayed via routem)
  ~12,000 different attribute combinations

## Slide 18: Update Packing

## Slide 19: Update Packing
With the ideal table we are able to pack the maximum number of prefixes into each update because all prefixes share a common set of attributes.
With the real world table we send updates that are not fully packed because we walk the table based on prefix but prefixes that are side by side may have different attributes. We can only walk the table for a finite amount of time before we have to release the CPU so we may not find all the NLRI for a give attribute combination before sending the updates we have built and suspending.
With 500 RRCs the ideal table takes ~4 minutes to converge where a real world table takes ~19 minutes!!

## Slide 20: UPDATE Packing
UPDATE packing bugs
BGP would pack one NLRI per update unless “set metric” was configured in an outbound route-map
  CSCdt81280 - BGP: Misc fixes for update-generation – 12.0(16.6)S
  CSCdv52271 - BGP update packing suffers with confederation peers – 12.0(19.5)S
Same fix but CSCdt81280 is for regular iBGP and CSCdv52271 is for confed peers

## Slide 21: UPDATE Packing
Example of CSCdt81280 from customer router
BGP has 132k routes and 26k attribute combinations
Took 130k messages to advertise 132k routes
132853 network entries and 1030454 paths using 49451673 bytes of memory
26184 BGP path attribute entries using 1361568 bytes of memory
Neighbor V AS MsgRcvd MsgSent TblVer InQ OutQ Up/Down State/PfxRcd
1.1.1.1 4 100 19 130681 354811 0 0 00:20:31 34
1.1.1.2 4 100 816 130782 354811 0 0 00:21:04 2676

## Slide 22: UPDATE Packing
CSCdt34187 introduces an improved update generation algorithm:
  100% update packing – attribute distribution no longer makes a significant impact
  100% peer-group replication – no longer have to worry about peers staying “in sync”

## Slide 23: UPDATE Packing
4x – 6x improvement!!

## Slide 24: UPDATE Packing
12.0(19)S + MTU discovery + Larger Input Queues = 14x improvement

## Slide 25: READ_ONLY Mode
READ_ONLY Mode - If BGP is in READ_ONLY mode then BGP is only accepting routing updates and is not computing a best path nor advertising routes for any prefixes. When the BGP process starts (i.e. after a router reboot) BGP will go into READ_ONLY mode for a maximum of two minutes. RO mode forces a BGP speaker to be still for a few minutes giving his peers a chance to send their initial set of updates. The more routes/paths BGP has the more stable the network will be because we will avoid the scenario where BGP sends an update for a prefix and then learns about a better path for that prefix a few seconds later. If that happened then BGP sent two updates for a single prefix, which is very inefficient. READ_ONLY mode increases the chances of BGP learning about the bestpath for a prefix before sending out any advertisements for that prefix. BGP will transition from RO mode to RW mode once all of our peers have sent us their initial set of updates or the two-minute RO timer expires.
READ_WRITE Mode - This is the normal mode of operation for BGP. While in READ_WRITE mode BGP will install routes in the routing table and will advertise those routes to his peers.

## Slide 26: READ_ONLY Mode
RO and RW modes were introduced via CSCdm56595
RO timer (120 seconds) started when BGP process started
Never worked on GSR because it takes more than 120 seconds for linecards to boot, IGP to converge, etc…

## Slide 27: READ_ONLY Mode
CSCds66429 corrects oversights made by CSCdm56595
RO timer now starts when the first peer comes up
  Linecard boot times and IGP convergence are accounted for automatically
Will transition to RW mode when one of the following happens:
  All peers have sent us a KA
  All peers that were up within 60 seconds of the first peer have sent us a KA. This way we do not wait 120s for a peer that is mis-configured
  The 120s timer pops

## Slide 28
What happened
to 12.0(21)S?

## Slide 29: Introduction
Customer demand for faster BGP convergence
  BGP could take over 60 minutes to converge 100+ peers
CSCdt34187 - BGP should optimize update advertisement
Committed to 12.0(18.6)S and 12.0(18)S1
Dramatically reduced convergence times and improved scalability
Known as “Init” mode convergence algorithm
  Pre- CSCdt34187 method is known as “Normal” mode

## Slide 30: How does it work?
CSCdt34187 improves convergence by achieving 100% update packing and 100% update replication
New algorithm is used to efficiently pack updates and replicate them to all peer-group members
BGP converges much faster but uses large amounts of transient memory to do so

## Slide 31: Oops
When memory is low, BGP will throttle itself to avoid running out of memory
The problem
  BGP does not have a low watermark in terms of how much memory it is allowed to use
  Can use the majority of memory but not all of it
  Other processes need more memory than BGP is leaving available
The result
  Customers running 12.0(18)S1 or 12.0(19)S saw extremely low watermarks in free mem
  Upgrading to 12.0(21)S almost always resulted in malloc fail on GSR
  12.0(21)S was deferred

## Slide 32: What is happening?
Any event that causes another process to use large amounts of transient memory while BGP is converging can result in a malloc failure
CEF XDR messages are the most common problem
XDRs are used to update linecards with information about the RIB/FIB
XDRs can consume a lot of memory

## Slide 33: XDR Triggers
When a linecard boots, XDRs are used to send it the RIB/FIB
  Linecards booting while BGP is trying to converge can result in malloc failure
  Upgrading from 12.0(19)S to 12.0(21)S will cause the linecards to boot one at a time because various software components on the linecards must be upgraded
  If it takes more that 2 minutes (default update-delay timer) for all linecards to boot then cards will be coming up while BGP is converging

## Slide 34: XDR Triggers
Any significant routing change can trigger a wave of XDRs
  A new peer comes up whose paths are better than the ones BGP currently has installed
  Must re-install new bestpaths which cause XDRs to be sent to all linecards

## Slide 35: XDR Triggers
Double recursive lookups almost always trigger a significant routing change
  A [AS 100, advertises 10.0.0.0/8]
  |
  |
  B ------------- C [B and C are in AS 200]
B does not do next-hop-self on session to C
Instead B does “redistribute connected” and “redistribute static” into BGP
C will know about A’s next-hop but will know about it via BGP

## Slide 36: XDR Triggers
  A [AS 100, advertises 10.0.0.0/8]
  |
  |
  B ------------- C [B and C are in AS 200]
Step 1 - C will transition from RO mode to RW mode
Step 2 - C will not have a route to A because he will only know about A via BGP but we haven’t installed any BGP routes
Step 3 - C will select some other route as best and install it. Other BGP routes, including the route to A, are installed at this point
Step 4 – BGP begins converging peers which uses most of the memory on the box
Step 5 - bgp_scanner runs on C but now A is reachable so C’s bestpath for 10.0.0.0/8 changes
Do this 100k times and you have a lot of XDR messages

## Slide 37: The Solution
Must take multiple steps to avoid malloc failure
#1- BGP has a RIB throttle mechanism that allows us to delay installing a route in the RIB if memory is low (). Avoids malloc failures during large routing changes like the double recursive scenario
#2 – CEF will wait for all linecards to boot before enabling CEF on any linecard. Avoids the problem of sending XDRs to slow booting linecards while BGP is trying to converge

## Slide 38: The Solution
#3 – If a linecard crashes/reboots while BGP is trying to converge CEF will signal BGP that it needs more transient memory to bring the linecard up. BGP will finish converging the current peer-group and will signal CEF that memory is available.
#4 – “Init” mode in BGP will always try to leave 20M free for CEF (distributed platforms only. An additional 1/32 of total memory on the box will be left free for other processes
#5 – BGP will fall back to Normal mode if we can’t converge without leaving required amounts of memory free

## Slide 39
<number>
www.cisco.com
CCIE ‘99 Session 1624
scsturge@cisco.com
© 1999, Cisco Systems, Inc.
Notes: <number>
<footer>
<header>
<date/time>